Documentation for ModVisc 0.01

by
Prof. Dr. Harro Schmeling
and
Jan Philipp Kruse

Universitiy of Frankfurt

Geodynamics

2012

Content:

1.	General information
2.	Parameter description
2.1	modulus
2.2	viscosities
3.	Plotting
3.1	modulus
3.2	viscosities
4.	Saving
4.1	matlab data files
4.2	txt files

1.	General information

 start model
 calculation
 delete model
 resp. models
 plot selected values

 plot model
 resp. models

Figure 1: example for calculating and plotting elastic moduli or seismic velocities
In Fig. 1 you can see how to use ModVisc 0.01. It is possible to switch between the calculation of elastic moduli or effective viscosities. The handling is for both tabs the same.

2.	Parameter description

2.1	Modulus

parameter name	description	default value
K0	Intrinsic bulk-modulus of the matrix	0,66
Kf	Intrinsic bulk-modulus of the fluid	0,2
μ0	Intrinsic shear-modulus of the matrix	0,4
φmin	Minimum value for melt fraction (zero is not allowed)	10-6
φmax	Maximum value for melt fraction (has to be smaller or equal to one; one means 100% melt fraction)	0,2 (20%)
φnum	Number of fraction values between φmin and φmax; realized with φ = logspace(log10(φmin), log10(φmax), φnum); for detailed information please read matlab documentation about logspace	1000
nmax	Tells maximum number of iterations which are allowed for each fraction value φ	1000
unit	Unit for the moduli; free choose is not allowed because seismic velocities are also calculated	MPa
ρ0	Intrinsic density of the matrix	3300 [kg m-3]
Δρ	Density difference between matrix and fluid; density for calculating the seismic velocities is given by / ρ = ρ0 – Δρ φ	300 [kg m-3]
films	Check if you want to include film geometry	unchecked
tubes	Check if you want to include tube geometry	unchecked
spheroids	Check if you want to include spheroid geometry	checked
model name	This name appears in the model table and in the legend for the case of plotting	model 1
α1	Aspect ratio of the oblate ellipsoidal films; / should be << 1 otherwise there will occur relative errors for K and μ which increase linear with melt fraction; detailed information are given in 1)	0,01
c1i	Relative fraction for isolated oblate ellipsoidal films; has to be a value between zero and one (zero means 0%, one means 100%); see *	0
c1c	Relative fraction for connected oblate ellipsoidal films; has to be a value between zero and one (zero means 0%, one means 100%); see *	0
κ	Shape parameter for the cross section of the tubes; value interval reachs from zero to infinity (choose a really large value); for detailed information see 1) resp. 2)	0
c2i	Relative fraction for isolated tubes; has to be a value between zero and one (zero means 0%, one means 100%); see *	0
c2c	Relative fraction for connected tubes; has to be a value between zero and one (zero means 0%, one means 100%); see *	0
α3	Aspect ratio of the oblate ellipsoidal spheroids; value has to be larger than zero and equal or smaller than 1 ( 0 < %alpha_3 leslant 1 )	0,1
c3i	Relative fraction for isolated oblate ellipsoidal spheroids; has to be a value between zero and one (zero means 0%, one means 100%); see *	0
c3c	Relative fraction for connected oblate ellipsoidal spheroids; has to be a value between zero and one (zero means 0%, one means 100%); see *	1

* the sum of all c's has to be 1

2.2	Viscosities

parameter name	description	default value
ηb0	Effective bulk-viscosity of the matrix is set to infinity, because matrix is incompressible; for detailed information see [1]	∞
ηbf	Effective bulk-viscosity of the fluid is set to zero, because effective bulk viscosity relates the dilatational strain rate to the isotropic part of the viscous stress tensor and not to the pore fluid pressure; for detailed information see [1]	0
ηs0	Intrinsic dynamic shear-viscosity of the matrix	1018
φmin	Minimum value for melt fraction (zero is not allowed)	10-6
φmax	Maximum value for melt fraction (has to be smaller or equal to one; one means 100% melt fraction)	0,2 (20%)
φnum	Number of fraction values between φmin and φmax; realized with φ = logspace(log10(φmin), log10(φmax), φnum); for detailed information please read matlab documentation about logspace	1000
nmax	Tells maximum number of iterations which are allowed for each fraction value φ	1000
unit	Unit for the viscosities; is set to SI-unit and not changeable	Pa s
films	Check if you want to include film geometry	unchecked
tubes	Check if you want to include tube geometry	unchecked
spheroids	Check if you want to include spheroid geometry	checked
model name	This name appears in the model table and in the legend for the case of plotting	model 1
α1	Aspect ratio of the oblate ellipsoidal films; / should be << 1 otherwise there will occur relative errors for ηb and ηs which increase linear with melt fraction; detailed information are given in 1)	0,01
c1	Relative fraction for oblate ellipsoidal films; has to be a value between zero and one (zero means 0%, one means 100%); see **	0
κ	Shape parameter for the cross section of the tubes; value interval reachs from zero to infinity (choose a really large value); for detailed information see 1) resp. 2)	0
c2	Relative fraction for tubes; has to be a value between zero and one (zero means 0%, one means 100%); see **	0
α3	Aspect ratio of the oblate ellipsoidal spheroids; value has to be larger than zero and equal or smaller than 1 ( 0 < %alpha_3 leslant 1 )	0,1
c3	Relative fraction for oblate ellipsoidal spheroids; has to be a value between zero and one (zero means 0%, one means 100%); see **	1

** c1 + c2 + c3 = 1 has to be fulfilled

3.	Plotting

You are able to plot the results of one or many models in one plotting window. Depending on whether you want to plot modulus or viscositiy models you can choose between different values to plot. All values are plotted against the total melt fraction φ.

3.1	Modulus

value	description
Ku	Unrelaxed bulk-modulus
Kr	Relaxed bulk-modulus
μu	Unrelaxed shear-modulus
μr	Relaxed shear-modulus
υu	Unrelaxed poisson-ratio
υr	Relaxed poisson-ratio
vpu	Velocity of p-waves calculated with unrealxed moduli
vpr	Velocity of p-waves calculated with realxed moduli
vsu	Velocity of s-waves calculated with unrealxed moduli
vsr	Velocity of s-waves calculated with realxed moduli
vpu/vsu	Ratio of the velocities calculated with unrelaxed moduli
vpr/vsr	Ratio of the velocities calculated with relaxed moduli

If you want to have for example Ku and Kr from one or from different models in one plot window you have to check these checkboxes and choose one model or by holding CTRL many models inside the model table. After that you have to press the plot button in the toolbar at the top of the program (see Fig. 1)

3.2	Viscosities

value	description
ηb	bulk-viscosity
ηs	shear-viscosity
υ	poisson-ratio

For the viscosities it is possible to plot bulk- and shear-viscosity in one plot window. There is even an option to plot only the important parts, because in some configurations the bulk- resp. shear-viscosity will rapidly decrease until the error boundary is reached. These values are not biased and maybe you don't want to plot them.

4.	Saving

It is possible to save the calculated models as a text file (*.txt) or as a Matlab file (*.mat).

4.1	matlab data files

ModVisc saves the calculated models internally as a structure (struct). So even when you choose more than one model for saving there will be only one mat file. This mat file contains all models in the form of a struct (see "help struct" in matlab). To import your saved data in Matlab two alternatives. On the one hand you can do it interactive with File > Import Data and on the other hand you can do it in the command line with the command:

>>load 'path/filename'
When the saved data contains moduli models the variable name is "mod_models", when the saved data contains viscosity models the variable name is "visc_models". The following table should give you an overview which